## Slide 1: Making things spin
A crash course
https://github.com/choltfo/HtN2019_Workshop

## Slide 2: Robotics & Automation
Sensors
Processors
Actuators
The World
We are here!
Things you can control
Things you cannot control
https://github.com/choltfo/HtN2019_Workshop

## Slide 3: About me
Waterloo Mechatronics Engineering, 3rd year
From Ottawa, ON
Long time hacker/maker
Builder of things for ~10 years
Former Hacksmith Industries co-op
https://choltfo.github.io/
https://github.com/choltfo/HtN2019_Workshop

## Slide 4: About me
https://github.com/choltfo/HtN2019_Workshop

## Slide 5: About me
https://github.com/choltfo/HtN2019_Workshop

## Slide 6: About me
Working on:
Bigger coil gun
Pneumatic biomimetic articulator
Tesla coil
Feel free to ask me about stuff after the workshop or during the break!
https://github.com/choltfo/HtN2019_Workshop
Notes: The one constant with all of these projects is that they involves the same problems as motor control. So let’s dive into that.

## Slide 7: What we’re going to be covering
Brushed DC motors
Brushless DC motors (BLDC)
Steppers
Servos
And how to run all of them
  In theory
  In practice
https://github.com/choltfo/HtN2019_Workshop

## Slide 8: A quick note on practicality…
With a few exceptions…
DIY motor drivers:
  Great learning experience!
  Someone already did it better
  Someone already did it cheaper
DIY motors:
  Great learning experience!
  Someone already did it better
  Someone already did it cheaper
https://github.com/choltfo/HtN2019_Workshop

## Slide 9: Glossary 1/2
Two mechanical parts:
Rotor
  Rotates (The spinny bit)
  Usually internal (But not always)
Stator
  Stays (The frame)
  Usually external (But not always)
https://github.com/choltfo/HtN2019_Workshop

## Slide 10: Glossary 2/2
Inductive kick:
  The tendency of inductors to create huge voltage spikes
  See Afrotechmds: https://www.youtube.com/watch?v=LXGtE3X2k7Y
  Also called “flyback voltage”
MOSFET:
  Metal-oxide-semiconductor-field-effect-transistor
  (Magically Obliterated Smoke and Fire Emitting Transistor)
  Technically: Voltage controlled resistor
  Practically: Voltage controlled switch
https://github.com/choltfo/HtN2019_Workshop
Notes: ANY QUESTIONS

## Slide 11: Brushed DC Motors
Mechanically switched electromagnet on the rotor
Permanent magnet on the stator
Speed: Fast
Price: Low
Weight: High
Power: Phone buzzers to power tools
Ease of use: High
https://github.com/choltfo/HtN2019_Workshop

## Slide 12: Brushed DC Motors
Speed = K E
Torque = K I
V = R I + E
https://github.com/choltfo/HtN2019_Workshop

## Slide 13: Brushed DC Motors (Picking a Motor)
Operating voltage
  Maximum speed = K*voltage
Torque/speed curve
  Available with every motor...
    If you look hard enough
  Max torque at stall (0 speed)
  0 torque at max speed
Maximum current
  How much current does your motor use when stalled?
  Determines your driver’s specs.
https://github.com/choltfo/HtN2019_Workshop

## Slide 14: Brushed DC Motors (In practice!)
Forward and reverse:
  Buy an H-bridge motor driver
Just forward:
  MOSFET and flyback diode
  Use PWM (analogWrite on Arduino)
https://github.com/choltfo/HtN2019_Workshop

## Slide 15: Brushed DC Motors (In theory!)
Making it spin in one direction:
  Give it juice.
  No, seriously. It’s that easy.
To speed control, use PWM!
  Turn it on and off really fast.
Flyback diodes or death!
https://github.com/choltfo/HtN2019_Workshop

## Slide 16: Brushed DC Motors (In theory!)
H bridge
  Forward/backwards
  Braking
  Coasting
  Speed control
  More complicated
  Use an H-bridge driver chip
    Either with the MOSFETs in it, or
    With connections to the gates of big MOSFETs
https://github.com/choltfo/HtN2019_Workshop
Notes: ANY QUESTIONS

## Slide 17: Brushless DC Motors
3-phase electrically switched electromagnets on stator
Permanent-magnet rotor
Speed: Very fast (>25,000 RPM)
Price: Medium
Weight: Low
Power: Tiny quadcopters to electric cars
Ease of use: Moderate to difficult
https://github.com/choltfo/HtN2019_Workshop

## Slide 18: Brushless DC Motors (Picking a Motor)
Operating voltage
  Maximum speed = K*voltage
  K = “Kv” rating (~1500 RPM/V)
Torque/speed curve
  A bit more complicated, but…
  Max torque at stall
  No torque at max speed
Maximum current
  Determines the driver you need
    When in doubt, multiply by 1.5
https://github.com/choltfo/HtN2019_Workshop

## Slide 19: Brushless DC Motors (In Practice!)
Buy an ESC (Electronic Speed Controller)
  Takes standard servo-motor PWM
  Might double as a 5V supply
  Battery on one side, motor on the other
  1A to >300A
  3V to >100V
Usually takes some tweaking
  Read the manual!
https://github.com/choltfo/HtN2019_Workshop

## Slide 20: Brushless DC Motors (In Practice!)
Actually a 3-phase synchronous AC motor
DC needs to be turned into AC
  Use three “half-bridges”
Creates a rotating magnetic field around the rotor
Progression of the field pulls along the rotor.
https://github.com/choltfo/HtN2019_Workshop

## Slide 21: Hobby Servo Motors
Provides a constant speed or position
Has its own tiny computer in it
Speed: Slow
Price: Varies
Weight: Varies
Power: Varies
Ease of use: High
https://github.com/choltfo/HtN2019_Workshop

## Slide 22: Hobby Servo Motors (In Practice!)
Connect the brown and red wires to GND and 5V
BROWN to GND
RED to 5V
Connect the yellow wire to a control pin
  Digital I/O pin on Arduino
Use a servo library (Servo.h on Arduino)
https://github.com/choltfo/HtN2019_Workshop

## Slide 23: Stepper Motors
Progress one increment/step at a time
Needs a stepper driver
Comes in bipolar and unipolar flavours
Four wires
https://github.com/choltfo/HtN2019_Workshop

## Slide 24: In practice
Two kinds of driver:
Cheap ones:
  Provides a connection to either ground or V+ for each pin according to the pins you have connected
  4-pin inputs
  Control is your problem!
Good ones:
  Handles all of the weirdness internally
  Microswitching
  Step/direction inputs
https://github.com/choltfo/HtN2019_Workshop

## Slide 25: Trying it live!
Brushed motor
  Arduino
  MOSFET
  Diode
  Motor
Stepper
  Stepper driver
  Arduino
  Stepper motor
  Read the comments in the examples
Servo:
  Arduino
  Wires (3)
  Servo motor
https://github.com/choltfo/HtN2019_Workshop

## Slide 26: Schematics
Unipolar stepper motor
Brushed DC motor
https://github.com/choltfo/HtN2019_Workshop